## Slide 1: End Node Schematics
By Souvik Halder

## Slide 2: END NODE BLOCK DIAGRAM
CLOCK
BLOCK
FREQ/2
GPS IC
RF transceiver - LR1120
SPI(4), BUSY
16MHz,
32MHz
UART(2), WAKEUP
32MHz
I2C(2)
EEPROM
2MB
FLASH
32MB
QSPI(I/O(4), nCS, SCK )
JTAG(5)
USB
USB(DM, DP)
JTAG
GPIO
POWER SUPPLY BLOCK
LR1120 RF TRANSCEIVER VOLTAGE
MCU SUPPLY(V_MCU)
GPIO : BERGSTRIPS(20)
GPS SUPPLY(V_GPS)
SPI
SPI(4)
MCU
STM32WB55CG
CORTEX M4
WITH BLE
32.867KHz
32.867KHz
APB1 BUS
WATCHDOG
TIMER
UART DEBUGGING
LR1120 RF ANTENNA
GPS ANTENNA
IMU SENSOR
IRQ
I2C
HALL EFFECT
USER BUTTON
GPIO
GPIO

## Slide 3: RF transceiver - LR1120
Unused
CLOCK SOURCE - TCXO BLOCK
TCXO BLOCK

## Slide 4: END NODE MCU SELECTION
STM32WB55CG:
Dual-core architecture: Features an Arm Cortex-M4 (application core) + Cortex-M0+ (network core), enabling clean separation between user app and wireless stack.
Built-in wireless: Native support for Bluetooth Low Energy (BLE 5.0/5.1) and IEEE 802.15.4 (Thread, Zigbee, proprietary).
Ultra-low power MCU: Optimized for battery-powered IoT with multiple low-power modes and very low sleep current.
Rich peripherals: Includes ADC, timers, SPI, I²C, USART, USB, RTC, DMA, and capacitive touch support.
Security features: Hardware cryptography (AES, PKA), secure boot, firmware upgrade, and TrustZone-like isolation via dual core.
Ideal for IoT nodes: Widely used in smart sensors, wearables, beacons, home automation, and industrial wireless nodes.

## Slide 5: LoRa Transceiver, GPS, BLE
GPS : Quectel L89
Multi-constellation GNSS: Supports NavIC (IRNSS) along with GPS, GLONASS, Galileo, and QZSS for improved positioning accuracy in India.
Low power operation: Optimized for battery-powered IoT devices with low tracking and acquisition power consumption and standby modes.
Simple host interface: UART interface with standard NMEA output, enabling easy integration with STM32-class microcontrollers.
Fast and accurate fixes: High-sensitivity receiver with quick TTFF (Time-To-First-Fix) and stable performance in weak-signal environments.
LoRa Transceiver : LR1120
Multi-band LoRa® transceiver: Supports sub-GHz and 2.4 GHz LoRa® RX/TX with ultra-low power operation, ideal for long-range, battery-powered IoT nodes.
LR-FHSS uplink support: Enables Long Range – Frequency Hopping Spread Spectrum for massive-scale networks, high capacity, and improved interference robustness.
Energy-efficient design: Very low RX current consumption with deep sleep modes, optimized for multi-year battery life in IoT deployments.
Advanced features for NTN & mobility: Supports Doppler tolerance, fine timestamping, and scalable data rates, making it suitable for LEO satellite (NTN) LoRaWAN use cases.
Tx power consumption can further be controlled using periodic uplinks and deep sleep with aid of LoRaWAN class B
BLE : ST32WB55CG INBUILT
Dedicated BLE core: BLE runs on a separate Cortex-M0+ network core, keeping the Cortex-M4 free for application tasks (no RTOS conflicts).
BLE 5.x compliant: Supports Bluetooth Low Energy 5.0/5.1 features like extended advertising, higher data rate, and improved range.
Pre-certified BLE stack: Comes with ST-provided, qualified BLE stack, reducing certification effort and time-to-market.
Low-power BLE operation: Optimized radio and sleep modes enable very low current consumption, ideal for battery-powered IoT nodes.
Secure wireless communication: Hardware-based AES encryption, pairing, bonding, and secure firmware update over BLE.

## Slide 6: Power Consumption and Battery

## Slide 7: MECHANICALS AND FITMENT